Confined Space Assessments

For

On Campus Grounds

Page #	Confined Space Location

2		Fish Pond Manhole

3		Manholes (sanitary/sewer)

CONFINED SPACE ASSESSMENT         Decision:  Permit Required   Non-Permit

| Building: On Campus Grounds Confined Space Location: Fish Pond Manhole Date of Assessment: September 10, 2003 Conducted By: | Purpose of Entry: Repair and maintenance |
| --- | --- |
| NO. 1 To determine if the space listed above is a confined space, highlight the response that best applies to the space being evaluated. |
| The space is large enough and is so configured that an employee can bodily enter and perform assigned work. | YES | NO |
| The space has limited or restricted means of entry or exit. (i.e. tanks, vaults, vessels, silos, storage bins, hoppers, pits, diked areas) | YES | NO |
| The space is not designed for continuous employee occupancy. | YES | NO |
| If ALL three of the above statements were answered YES, the area being evaluated is a CONFINED SPACE. Continue to the next section to determine if it is a “PERMIT-REQUIRED” confined space. If ANY of the above statements were answered NO, check the following box and proceed no further. The area does not qualify as a “confined space.” |
| NO. 2 Use the following section to determine if it is a “permit-required” confined space. |
| The space contains, or has the potential to contain a “hazardous atmosphere”. Check all those that apply. | YES | NO |
| ______ Flammable gas / vapor / mist Fuel supply locked out/disconnected | ____ Oxygen conc. below 19.5% or above 23.5% |
| _____ Airborne combustible dust conc. > or = its LFL. Dust obscures vision @ 5 feet or less. | _____ Atmospheric concentration exceeding the PEL or dose for any substance published in subpart G or Z. |
| ______ Any other atmospheric condition that is IDLH. (i.e. poor ventilation, migrating vapors / gases) | _____ Other: (inerting gases, etc) |  |
| The space contains a material that has the potential for engulfing an entrant (i.e. fill or plug respiratory tract, cause death by crushing, constriction or strangulation) | YES | NO |
| The space has an internal configuration such that an entrant could become trapped or asphyxiated. Check all those that apply. | YES | NO |
| _____ Converging walls / downward sloping floors | _____ Constriction / taper to a smaller cross-section |
| _____ Difficult to exit / inadequate access / obstacles | _____ Other: |  |  |  |
| The space contains other recognized serious safety or health hazards. Highlight yes or no, then check all those that apply. | YES | NO |
| _____ Poor or difficult communication |  | _____ Noise / vibration |  |  |
| _____ Equipment startup / mechanical hazard | _____ Inadequate light / poor visibility |  |
| _____ Hot or cold contact / extremes |  | _____ Slip & trip surfaces, fall from heights |  |
| _____ Electrical shock | Water? | Lights | _____ Sharp objects / falling objects |  |
| _____ Release of stored & hazardous energy | _____ Unknown contents / sludge / residue |
| _____ Flooding / avalanche of materials / engulfment | _____ Radiation |  |  |
| _____ Toxic chemicals |  |  | _____ Atmospheric contaminant |  |
| _____ Corrosive materials |  |  | _____ Chemical reactivity |  |  |

CONFINED SPACE ASSESSMENT         Decision:  Permit Required   Non-Permit

| Building: On Campus Grounds Confined Space Location: Manholes (sanitary/sewer) Date of Assessment: September 10, 2003 Conducted By: | Purpose of Entry: Repair and maintenance |
| --- | --- |
| NO. 1 To determine if the space listed above is a confined space, highlight the response that best applies to the space being evaluated. |
| The space is large enough and is so configured that an employee can bodily enter and perform assigned work. | YES | NO |
| The space has limited or restricted means of entry or exit. (i.e. tanks, vaults, vessels, silos, storage bins, hoppers, pits, diked areas) | YES | NO |
| The space is not designed for continuous employee occupancy. | YES | NO |
| If ALL three of the above statements were answered YES, the area being evaluated is a CONFINED SPACE. Continue to the next section to determine if it is a “PERMIT-REQUIRED” confined space. If ANY of the above statements were answered NO, check the following box and proceed no further. The area does not qualify as a “confined space.” |
| NO. 2 Use the following section to determine if it is a “permit-required” confined space. |
| The space contains, or has the potential to contain a “hazardous atmosphere”. Check all those that apply. | YES | NO |
| ______ Flammable gas / vapor / mist Fuel supply locked out/disconnected | ____ Oxygen conc. below 19.5% or above 23.5% |
| _____ Airborne combustible dust conc. > or = its LFL. Dust obscures vision @ 5 feet or less. | _____ Atmospheric concentration exceeding the PEL or dose for any substance published in subpart G or Z. |
| __X___ Any other atmospheric condition that is IDLH. (i.e. poor ventilation, migrating vapors / gases) | _____ Other: (inerting gases, etc) |  |
| The space contains a material that has the potential for engulfing an entrant (i.e. fill or plug respiratory tract, cause death by crushing, constriction or strangulation) | YES | NO |
| The space has an internal configuration such that an entrant could become trapped or asphyxiated. Check all those that apply. | YES | NO |
| _____ Converging walls / downward sloping floors | _____ Constriction / taper to a smaller cross-section |
| _____ Difficult to exit / inadequate access / obstacles | _____ Other: |  |  |  |
| The space contains other recognized serious safety or health hazards. Highlight yes or no, then check all those that apply. | YES | NO |
| __X__ Poor or difficult communication |  | _____ Noise / vibration |  |  |
| _____ Equipment startup / mechanical hazard | __X__ Inadequate light / poor visibility |  |
| _____ Hot or cold contact / extremes |  | _____ Slip & trip surfaces, fall from heights |  |
| _____ Electrical shock | Water? | Lights | _____ Sharp objects / falling objects |  |
| _____ Release of stored & hazardous energy | __X__ Unknown contents / sludge / residue |
| _____ Flooding / avalanche of materials / engulfment | _____ Radiation |  |  |
| __X__ Toxic chemicals |  |  | __X__ Atmospheric contaminant |  |
| _____ Corrosive materials |  |  | _____ Chemical reactivity |  |  |